## Slide 1: PinK: High-speed In-storage Key-value Store with Bounded Tails
ATC 2020
Junsu Im, Jinwook Bae, Chanwoo Chung*, Arvind*, and Sungjin Lee
Daegu Gyeongbuk Institute of Science & Technology (DGIST) *
Massachusetts Institute of Technology (MIT)
Presented by Qingyuan Chen and Yuming Xu, USTC, ADSL
November 11st, 2020
2020/4/17

## Slide 2: Outline
Motivation & Background
Design
Evaluation
Conclusion
2020/4/17
Notes: 接下来讲一下我们的研究内容

## Slide 3: Outline
Motivation & Background
Design
Evaluation
Conclusion
2020/4/17
Notes: 接下来讲一下我们的研究内容

## Slide 4: Key-Value System
20%
80%
Blooming unstructured data
Key-Value System
Key
Value
Notes: SSD结构

## Slide 5: Key-Value Storage Device
Host Key-Value Engine
Key-Value Interface
Block-SSD
Fewer Host Resources
Low Latency
High Throughput
KV-SSD
Key-Value Interface
CPU
Bottle neck
SSD access
Kvell(sosp 19)
KV system
Bottleneck move to cpu overhead KVell(sosp 19)

## Slide 6: KV-SSD
What’s their Problem ?
Provides the key-value interface
  Key and value are both of variable sizes
  Support a rich set of operations like iterations, range queries
Challenge :
  Limited DRAM & CPU capability
  Redesign of the FTL ( flash translation layer )
Implementation
  Academia
                KAML (HPCA’17), NVMKV(ATC’15), Bluecache (VLDB’16)，LightStore (ASPLOS’19)，iLSM-SSD (MASCOTS’19)
  Industry
                Samsung’s KV-SSD
SSD : 4TB, DRAM : 4GB ( 0.1% )

## Slide 7: Hash-based SSD Experiments
Samsung’s KV-SSD prototype
  Hash-based SSD
Benchmark
  Key and Value sizes : Average 32B and 1KB
Conclude
  long tail latency
  inconsistent read latency
What’s the reason?
Notes: random GET() requests on these KV pools for 10 minutes
KV pools ranging in size from1GB to 3TB

## Slide 8: Problem of Hash-based KV-SSD
Huge Hash Table
  All hash table on DRAM : 144GB DRAM needed
  Using signature : blooming conflict
Using signature
  inconsistent read latency
    Store more, conflicts more, flash access more
  long tail latency
    Signature conflict result unpredictable flash access
Cannot efficiently support iterations and range operations
SSD : 4TB, DRAM : 4GB
Key : 32B, Value : 1KB

## Slide 9: LSM-tree
L2 index
L3 index
2-properties
  Each level, KV objects are unique and kept sorted
  Due to overwrites, there are overlaps between levels
DRAM
Flash
L0
L2
L1
4
33
15
51
2
7
52
60
1
3
7
10
33
39
51
60
High
Low
LSM-tree Structure

## Slide 10: LSM-tree
L2 index
L3 index
2-properties
  Each level, KV objects are unique and kept sorted
  Due to overwrites, there are overlaps between levels
DRAM
Flash
L0
L2
L1
4
33
15
51
2
7
52
60
1
3
7
10
33
39
51
60
GET(39)
High
Low
Once GET() come
Bloom filter

## Slide 11: LSM-tree
L2 index
L3 index
2-properties
  Each level, KV objects are unique and kept sorted
  Due to overwrites, there are overlaps between levels
DRAM
Flash
L0
L2
L1
4
33
15
51
2
7
52
60
1
3
7
10
33
39
51
60
GET(39)
High
Low
Once GET() come
Bloom filter

## Slide 12: LSM-tree
DRAM
Flash
L0
L2
L1
4
33
15
51
2
7
52
60
1
3
7
10
33
39
51
60
flush
High
Low
Once L0 Full
Flush & Compaction

## Slide 13: LSM-tree
DRAM
Flash
L0
L2
L1
1
2
3
4
7
10
15
33
High
Low
39
51
52
60
After Flush & Compaction
Low DRAM requirement
Support range and scan operations
worst-case latency of LSM-tree is bounded
Good enough?

## Slide 14: LSM-based SSD Experiments
Lightstore: LSM-tree-based KV-SSD
  Improve Bloom filter
Benchmark
  Lightstore: YCSB-LOAD(100%write) and YCSB-C (100%Read), 32B key and 1KB value

## Slide 15: Problem of LSM-based KV-SSD
Long tail latency
  probabilistic nature of Bloom filter
CPU overhead
  Rebuild Bloom filer
  Merge sort at compaction
I/O overhead
  I/O at compaction

## Slide 16: Outline
Motivation & Background
Design
Evaluation
Conclusion
2020/4/17
Notes: 接下来讲一下我们的研究内容

## Slide 17: Design of PinK
Overview
Level Pinning
Optimizing Search Path
Compaction Speed Up
Optimizing GC
Durability and Scalability Issues
2020/4/17
Notes: 接下来讲一下我们的研究内容

## Slide 18: Overview
PinK is based on key-value separated LSM-tree
Key-Value Separated LSM-tree

## Slide 19: Level Pinning
PinK keeps meta segments of K levels in DRAM
Move K levels’ meta segment into DRAM
Read worst case:Only need O(h-1-k) Flash access to get value

## Slide 20: Level Pinning
PinK keeps meta segments of K levels in DRAM
Memory Requirement？
Assume that an SSD capacity is 4TB and each meta segment is 16KB
And average sizes of keys and values are 32B and 1KB
Meta segment size for L1,L2,L3,L4:
0.91MB,50.86MB,2.83GB,161.63GB
4GB DRAM(0.1% of SSD capacity) can hold L1-L3

## Slide 21: Level Pinning
PinK keeps meta segments of K levels in DRAM
Reduce Compaction I/O
meta segments are in DRAM, don’t have to access flash，just update it directly
Dirty segments don’t have to write back to flash due to extra capacitors

## Slide 22: Optimizing Search Path
Stop using Bloom Filter
Use prefix of a key to reduce string comparison
Set a range pointer in each entry

## Slide 23: Optimizing Search Path
Stop using Bloom Filter
Reduce CPU overhead
Use prefix of a key to reduce string comparison
Add extra a prefix of a key(4B) in level list

## Slide 24: Optimizing Search Path
Set a range pointer in each entry
reduce search ranges of the level lists by borrowing fractional cascading technique
Level h-1 doesn’t maintain range pointer
说明

## Slide 25: Optimizing Search Path
Set a range pointer in each entry
说明
Memory Requirement: extra 43.9MB(10%)

## Slide 26: Compaction Speed Up
Move Compaction From CPU to HW accelerator in SSD controller

## Slide 27: Optimizing GC
Optimizing GC by reinserting valid data to LSM-tree

## Slide 28: Durability and Scalability Issues
Capacitor Limitation
PinK can address this issue by regularly writing data structures that reside in DRAM into flash
DRAM Scalability
One option is reduce the levels which are kept in DRAM
Another is reduce the height of the tree

## Slide 29: Design conclusion
Long tail latency
Level-pinning
CPU overhead
Remove Bloom filter
Optimize binary search
Adopt HW accelerator
I/O overhead
Reduce compaction I/O
Optimize GC

## Slide 30: Outline
Motivation & Background
Design
Evaluation
Conclusion
2020/4/17
Notes: 接下来讲一下我们的研究内容

## Slide 31: Setup
All algorithms for KV-SSD were implemented on ZCU102 board
For fast experiments: 64GB SSD, 64 MB DRAM (0.1% of NAND capacity)
Benchmark
YCSB, key: 32B, value: 1KB, first using load to create 44GB KV pool
 | Load | A | B | C | D | E | F
R/W | 0:100 | 50:50 | 95:5 | 100:0 | 95:5 | 95:5 | 50:50
Query Type | Point |  |  |  |  | Range | Point
Request Distribution | Uniform | Zipfan |  |  | Latest | Zipfian | 

## Slide 32: Testing Algorithms
Hash: 8-bit signature: total 320MB buckets
LSM-tree: based on Lightstore, total 5 levels (1~4 in flash)
Pink: Total 5 levels (only 4 in flash, rest pinned in DRAM)
Pink+HW: using HW accelerator
 | Hash | LSM-tree | Pink, Pink+HW
64MB DRAM | LRU bucket caching (64MB) | Level list (9MB) Bloom filter (55MB) | Level list + prefix range (10MB) Level-pinning (54MB)

## Slide 33: YCSB Throughput

## Slide 34: YCSB Read latency

## Slide 35: Level Pinning

## Slide 36: Search Path Optimization
PinK(NO-OPT): PinK without prefix and range pointer

## Slide 37: Level-pinning on Higher LSM-tree
Keep DRAM in 64MB but change the height of LSM-tree
Benchmark:YCSB-C (all read query)
LSM-tree(Monkey)
Pink

## Slide 38: Outline
Motivation & Background
Design
Evaluation
Conclusion
2020/4/17
Notes: 接下来讲一下我们的研究内容

## Slide 39: Conclusion
Goal: improve the performance of LSM-tree based KV-SSD
Long tail latency
CPU overhead
I/O overhead

## Slide 40: Conclusion
Approach
Another way
Level Pinning instead of using Bloom Filter
Space-Time Trade
Search Optimizing
Offload CPU
Move merge from CPU to HW accelerator
Optimize GC
In stead of updating meta segment which will cause a lot of flash read, reinsert KV pair

## Slide 41
2020/4/17
PinK:
High-speed In-storage Key-value Store with Bounded Tails
Thanks & QA!
November 11st, 2020